## Slide 1: ANNA: Specialized Architecture for Approximate Nearest Neighbor Search
Yejin Lee | Hyunji Choi | Sunhong Min | Hyunseung Lee
yejinlee@snu.ac.kr | hyunjichoi@snu.ac.kr | sunhongmin@snu.ac.kr | hs_lee@snu.ac.kr
Sangwon Beak | Dawoon Jeong | Jae W. Lee | Tae Jun Ham
bsw1907@gmail.com | daun20211@snu.ac.kr | jaewlee@snu.ac.kr | ham.taejun@gmail.com

## Slide 2: What is Nearest Neighbor Search (NNS)?
Recommender System
CTR Prediction Model
Search Engine
Click-Through-Rate
Also known as Similarity Search

## Slide 3: What is Nearest Neighbor Search (NNS)?
Modern algorithms and neural network models represent
  An entity  A learned high-dimensional vector called embedding
Image
Video
Word
Image embedding
Video embedding
Word embedding
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
-0.3 | 3.12 | 9.10 | 3.01
0.12 | 0.74 | -0.3 | 2.15 | 0.96

## Slide 4: What is Nearest Neighbor Search (NNS)?
Finding a set of embeddings that are the most similar to the query embedding
Image Embeddings
Video Embeddings
Word Embeddings
Query Image Embedding
Query Video Embedding
Query Word Embedding
What is the most similar
image embedding to the query image?
What is the most similar video embedding to the query video?
What is the most similar
word embedding to the query word?
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.12 | 0.74 | -0.3 | 2.15 | 0.96
-0.3 | 3.12 | 9.10 | 3.01
-0.3 | 3.12 | 9.10 | 3.01
-0.3 | 3.12 | 9.10 | 3.01
-0.3 | 3.12 | 9.10 | 3.01
-0.3 | 3.12 | 9.10 | 3.01
-0.3 | 3.12 | 9.10 | 3.01
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
0.43 | -0.2 | 1.54 | 8.21 | -4.2 | 1.49
-0.3 | 3.12 | 9.10 | 3.01
0.12 | 0.74 | -0.3 | 2.15 | 0.96
0.4 | 5.12 | 0.12 | 0.1 | 1.45
0.7 | 1.2 | 11.9 | -0.3
0.12 | -0.1 | 4.12 | 1.43 | -2.0 | 1.5

## Slide 5: Nearest Neighbor Search (NNS) Problem
Finding top-k vectors in a given database vectors that are the most similar to the query vector
What does similar mean?
  Inner product similarity
  L2 distance similarity

## Slide 6: Nearest Neighbor Search (NNS) Library
Existing popular libraries implements Approximate Nearest Neighbor Search
ANNS require ↓ computation and ↓ memory accesses at the expense of slight reduction in search accuracy

## Slide 7: Approximate Nearest Neighbor Search
Compression-based schemes are the most popular choice for billion-scale search
  Process with the compressed data  Fits necessary data in the main memory
  Efficient index structure
Nearest Neighbor Search
Exhaustive NNS
Approximate NNS
Graph-based
Hash-based
Compression-based

## Slide 8: Limitations on Conventional HW
Redundant data load from the memory (No reuse of the data)
Incurs unnecessary memory access & BW consumption ↑
Cannot support sub-byte data types effectively Incurs extra energy overhead & Throughput ↓
CPU (Intel Skylake-X)
Large amount of shared memory usage limits the GPU parallelism
Limit # of thread blocks to be scheduled on SM
Low arithmetic intensity
Resource Underutilization
GPU (NVIDIA V100)
We present ANNA, a specialized HW for billion-sale compression-based ANNS,
which flexibly supports various algorithms and configurations
Highly optimized datapath & data communication
Scalable extensions for throughput improvement
Fine-grained pipelining
Memory traffic optimization

## Slide 9: Two-level Product Quantization: Encoding
Encoding
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
1 | 4 | 5 | -2 | -1 | 7
9 | 3 | 1 | 7 | -1 | 4

## Slide 10: Two-level Product Quantization: Encoding
Encoding
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
-1 | 2 | 5 | -9 | 3 | 6
9 | 3 | 1 | 7 | -1 | 4
6 | 7 | 1 | 2 | -1 | -2
9 | 3 | 1 | 7 | -1 | 4
0 | -2 | 4 | -5 | 5 | 3
9 | 3 | 1 | 7 | -1 | 4
Cluster 0
Cluster 1
Cluster 2
Cluster 3

## Slide 11: Two-level Product Quantization: Encoding
Encoding
Residual
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
-10 | -2 | 4 | -15 | 4 | 2
9 | 3 | 1 | 7 | -1 | 4
-2 | 10 | -1 | -3 | 1 | -7
9 | 3 | 1 | 7 | -1 | 4
-9 | -4 | 3 | -10 | 6 | -1
9 | 3 | 1 | 7 | -1 | 4
Residual
Residual
Residual
1 | 4 | 5
1 | 4 | 5
1 | 4 | 5
1 | 4 | 5
1 | 4 | 5
9 | 3 | 1
9 | 3 | 1
0 | 1 | 3
9 | 3 | 1
3 | 3 | 1
9 | 3 | 1
0 | 1 | 1
0 | 2 | 1
Encode
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
1 | 4 | 5 | -2 | -1 | 7
9 | 3 | 1 | 7 | -1 | 4
9 | 3 | 1 | 7 | -1 | 4
-1 | 2 | 5 | -9 | 3 | 6
9 | 3 | 1 | 7 | -1 | 4
6 | 7 | 1 | 2 | -1 | -2
9 | 3 | 1 | 7 | -1 | 4
0 | -2 | 4 | -5 | 5 | 3
17 | 12 | 6 | 13 | -4 | 12
Cluster 0
Cluster 1
Cluster 2
Cluster 3

## Slide 12: Two-level Product Quantization: Encoding
Encoding
❶ -dimensional vector
Concatenation of M sub-vectors
,,, … ,
where is -dimensional vector
❶ Split into M=3
sub-vectors
D = 6
1 | 7
-1 | 4
9 | 3
9 | 3 | 1 | 7 | -1 | 4

## Slide 13: Two-level Product Quantization: Encoding
8 | 3
6 | 2
11 | 1
8 | 5
0 | 4
0 | 9
1 | 7
2 | 6
-2 | 5
0 | 4
2 | 7
3 | 5
0
1
2
3
k*=4
Codebook
Encoding
Codebook
Codebook
Codebook, , … ,, is obtained by separate training/learning process
Codebook = codewords
Sub-vector is encoded into an identifier using a codebook
❶ Split into M=3
sub-vectors
D = 6
1 | 7
-1 | 4
9 | 3
9 | 3 | 1 | 7 | -1 | 4

## Slide 14: Two-level Product Quantization: Encoding
s(r1(x), B1[0]) | = | -10
s(r1(x), B1[1]) | = | -5
s(r1(x), B1[2]) | = | 0
s(r1(x), B1[3]) | = | -2
s(r1(x), B1[2]) | = | 0
s(r2(x), B2[0]) | = | -2
s(r2(x), B2[1]) | = | -1
s(r2(x), B2[2]) | = | -18
s(r2(x), B2[3]) | = | -17
s(r0(x), B0[0]) | = | -1
s(r0(x), B0[1]) | = | -10
s(r0(x), B0[2]) | = | -8
s(r0(x), B0[3]) | = | -5
8 | 3
6 | 2
11 | 1
8 | 5
-2 | 5
0 | 4
2 | 7
3 | 5
0
1
2
3
0 | 4
8 | 3
k*=4
Codebook
❷ Compute
similarity
Encoding
❷ Compute
similarity
Codebook
Codebook
❷ Compute
similarity
❷ Computes similarity between
a sub-vector and
each codeword vector in codebook
Codeword with the highest similarity is selected
s(r0(x), B0[0]) | = | -1
s(r2(x), B2[1]) | = | -1
0 | 4
0 | 9
1 | 7
2 | 6
1 | 7
❶ Split into M=3
sub-vectors
D = 6
1 | 7
-1 | 4
9 | 3
9 | 3 | 1 | 7 | -1 | 4

## Slide 15: Two-level Product Quantization: Encoding
Encoding
❸ Assume is selected for , encoding identifier is
0 | 2 | 1
❸ Encode
Original vector = 2D bytes
Encoded vector = bytes
Vector : 12 bytes  bytes
❶ Split into M=3
sub-vectors
D = 6
1 | 7
-1 | 4
9 | 3
9 | 3 | 1 | 7 | -1 | 4
s(r1(x), B1[0]) | = | -10
s(r1(x), B1[1]) | = | -5
s(r1(x), B1[2]) | = | 0
s(r1(x), B1[3]) | = | -2
s(r1(x), B1[2]) | = | 0
s(r2(x), B2[0]) | = | -2
s(r2(x), B2[1]) | = | -1
s(r2(x), B2[2]) | = | -18
s(r2(x), B2[3]) | = | -17
s(r0(x), B0[0]) | = | -1
s(r0(x), B0[1]) | = | -10
s(r0(x), B0[2]) | = | -8
s(r0(x), B0[3]) | = | -5
8 | 3
6 | 2
11 | 1
8 | 5
-2 | 5
0 | 4
2 | 7
3 | 5
0
1
2
3
0 | 4
8 | 3
k*=4
Codebook
❷ Compute
similarity
❷ Compute
similarity
Codebook
Codebook
❷ Compute
similarity
s(r0(x), B0[0]) | = | -1
s(r2(x), B2[1]) | = | -1
0 | 4
0 | 9
1 | 7
2 | 6
1 | 7

## Slide 16: Two-level Product Quantization: Search
1 | 4 | 5
1 | 4 | 5
1 | 4 | 5
1 | 4 | 5
1 | 4 | 5
9 | 3 | 1
9 | 3 | 1
0 | 1 | 3
9 | 3 | 1
3 | 3 | 1
9 | 3 | 1
0 | 1 | 1
2 | 1 | 0
Cluster 0
Cluster 1
Cluster 2
Cluster 3
Search Process

## Slide 17: Two-level Product Quantization: Search
Computation
Given a query vector , find the most similar centroids by computing for all centroid vectors
= the set of selected centroids e.g.,
Search Process: Step 1- Cluster Filtering
=6
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
= | -2
= | -44
= | -5
= | -74
 | -2
 | -44
 | -5
 | -74
 | 9 | 3 | 1 | 7 | -1 | 4
 | 9 | 3 | 1 | 7 | -1 | 4
C (set of centroids)
9 | 4 | 1 | 6 | -1 | 4
9 | 2 | 1 | 5 | -1 | 4
Step 1. Cluster Filtering
Precompute
Precompute
: multiply-and-add operations
: multiply-and-add & addition
lookup &
addition
Similarity Computation

## Slide 18: Two-level Product Quantization: Search
, memoize
, memoize
2 | 3
0 | -1
1 | -7
8 | 9
Search Process: Step 2- Lookup Table Construction
=6
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 3 | 1 | 7 | -1 | 4
 | 9 | 3 | 1 | 7 | -1 | 4
C (set of centroids)
9 | 4 | 1 | 6 | -1 | 4
9 | 2 | 1 | 5 | -1 | 4
0
1
2
3
0 | -1
3 | 1
8 | 9
-6 | 4
4 | 2
-7 | 8
1 | 0
3 | 1
0 | 1
0 | 0
0 | -1
k*=4
-20
0
-37
-164
-4
-9
-128
-45
M=3
-20
-113
-1
-10
Step 2. Lookup Table Construction
Step 1. Cluster Filtering
 | = | -20
 | = | -113
 | = | -1
 | = | -10
 | = | -20
 | = | -113
 | = | -1
 | = | -10
 | = | -20
 | = | 0
 | = | -37
 | = | -164
 | = | -20
 | = | 0
 | = | -37
 | = | -164
 | = | -4
 | = | -9
 | = | -128
 | = | -45
 | = | -4
 | = | -9
 | = | -128
 | = | -45

## Slide 19: Two-level Product Quantization: Search
1 | 2 | 1
3 | 3 | 2
0 | 1
0 | 0
0 | -1
Search Process: Step 3 – Similarity Computation Using Memoization
=6
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 3 | 1 | 7 | -1 | 4
 | 9 | 3 | 1 | 7 | -1 | 4
C (set of centroids)
9 | 4 | 1 | 6 | -1 | 4
9 | 2 | 1 | 5 | -1 | 4
M=3
Cluster 0
0 | 1 | 3
-20
0
-37
-164
-4
-9
-128
-45
-20
-113
-1
-10
Step 2. Lookup Table Construction
Step 3. Similarity Computation
Each similarity computation only takes M lookups and M additions
Step 1. Cluster Filtering

## Slide 20: Two-level Product Quantization: Search
Each similarity computation only takes M lookups and M additions
1 | 2 | 1
3 | 3 | 2
0 | 1
0 | 0
0 | -1
=6
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 3 | 1 | 7 | -1 | 4
 | 9 | 3 | 1 | 7 | -1 | 4
C (set of centroids)
9 | 4 | 1 | 6 | -1 | 4
M=3
Cluster 0
0 | 1 | 3
-20
0
-37
-164
-4
-9
-128
-45
-20
-113
-1
-10
Search Process: Step 3 – Similarity Computation Using Memoization
Step 2. Lookup Table Construction
Step 3. Similarity Computation
Step 1. Cluster Filtering

## Slide 21: Two-level Product Quantization: Search
-8
-4
-65
-128
-9
-10
-113
-40
-20
-113
-1
-10
Step 2-3 is repeated for all vectors in the selected clusters
3 | 2 | 2
1 | 3 | 2
0 | 2
0 | 0
0 | 1
=6
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 3 | 1 | 7 | -1 | 4
 | 9 | 3 | 1 | 7 | -1 | 4
C (set of centroids)
9 | 4 | 1 | 6 | -1 | 4
M=3
Cluster 2
0 | 1 | 1
Step 3. Similarity Computation
=-242
45
9 | 2 | 1 | 5 | -1 | 4
Search Process: Step 3 – Similarity Computation Using Memoization
Step 2. Lookup Table Construction
Step 1. Cluster Filtering

## Slide 22: Two-level Product Quantization: Search
3 | 2 | 2
1 | 3 | 2
0 | 2
0 | 0
0 | 1
Select the top-k most similar vectors among dataset vectors in selected clusters
=6
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
 | 9 | 4 | 1 | 6 | -1 | 4
 | 8 | -3 | 2 | 5 | -2 | 5
 | 9 | 2 | 1 | 5 | -1 | 4
 | 8 | 9 | 5 | 6 | -3 | 8
Step 1. Cluster Filtering
 | 9 | 3 | 1 | 7 | -1 | 4
 | 9 | 3 | 1 | 7 | -1 | 4
C (set of centroids)
9 | 4 | 1 | 6 | -1 | 4
M=3
Step 2. Lookup Table Construction
0 | 1 | 1
Step 3. Similarity Computation
9 | 2 | 1 | 5 | -1 | 4
-8
-4
-65
-128
-9
-10
-113
-40
-20
-113
-1
-10
Search Process: Step 4 –Top-k selection
-242
-45
-131
1 | 2 | 1
3 | 3 | 2
0 | 1 | 3
-241
-211
-39
Cluster 2
Step 4. Top-k Selection
Cluster 0
Top-k
-39, -45

## Slide 23: ANNA: Specialized Architecture for ANNS
ANNA: Approximate Nearest Neighbor search Accelerator which can accelerate modern billion-scale ANNS algorithms
  Faiss ScaNN
ANNA substantially improve throughput and energy efficiency while flexibly supporting various search configurations (e.g., Search metrics, , , )

## Slide 24: ANNA: Specialized Architecture for ANNS
Compute Unit (CU)
Compute Unit (CU) 1
Memory Reader
Encoded
Vector
Buffer
Register
Encoded Vector Fetch
Module (EFM)
Memory Reader
Memory Reader
metric
0
Codebook
query
SRAM
To/From MAI
Arb
Compute Unit (CU) 0
Reduction
Unit
Unpacker
Top k
Unit
Top k
Unit
Cluster/Codebook Processing Module (CPM)
Similarity Computation Module
(SCM)
…
Lookup
Table
MAI (Memory Access Interface)
1. Memory Reader reads centroid vectors in a streaming manner
2. Compute Units compute similarity between the query and centroid
3. Computed similarities are passed to the Top-k selection unit
Search Process: Step 1 - Cluster Filtering
Inner Product
L2 Distance

## Slide 25: ANNA: Specialized Architecture for ANNS
Compute Unit (CU)
Compute Unit (CU) 1
Memory Reader
Encoded
Vector
Buffer
Register
Encoded Vector Fetch
Module (EFM)
Memory Reader
Memory Reader
metric
0
Codebook
query
SRAM
To/From MAI
Arb
Compute Unit (CU) 0
Reduction
Unit
Unpacker
Top k
Unit
Top k
Unit
Cluster/Codebook Processing Module (CPM)
Similarity Computation Module
(SCM)
…
Lookup
Table
MAI (Memory Access Interface)
1. Read codewords from Codebook SRAM
2. Only for L2 Distance Compute residual
3. Compute value for lookup table
Search Process: Step 2 – Lookup Table Construction
Inner Product
L2 Distance

## Slide 26: ANNA: Specialized Architecture for ANNS
Compute Unit (CU)
Compute Unit (CU) 1
Memory Reader
Encoded
Vector
Buffer
Register
Encoded Vector Fetch
Module (EFM)
Memory Reader
Memory Reader
metric
0
Codebook
query
SRAM
To/From MAI
Arb
Compute Unit (CU) 0
Reduction
Unit
Unpacker
Top k
Unit
Top k
Unit
Cluster/Codebook Processing Module (CPM)
Similarity Computation Module
(SCM)
…
Lookup
Table
MAI (Memory Access Interface)
Search Process: Step 3 – Similarity Computation Using Memoization
1. [EFM] Loads encoded vectors within a set of selected clusters & Unpacks and store in the buffer

## Slide 27: ANNA: Specialized Architecture for ANNS
Compute Unit (CU)
Compute Unit (CU) 1
Memory Reader
Encoded
Vector
Buffer
Register
Encoded Vector Fetch
Module (EFM)
Memory Reader
Memory Reader
metric
0
Codebook
query
SRAM
To/From MAI
Arb
Compute Unit (CU) 0
Reduction
Unit
Unpacker
Top k
Unit
Top k
Unit
Cluster/Codebook Processing Module (CPM)
Similarity Computation Module
(SCM)
…
Lookup
Table
MAI (Memory Access Interface)
Search Process: Step 3 – Similarity Computation Using Memoization
2. [SCM] Reads encoded identifies & Retrieve value from the Lookup Table
1. [EFM] Loads encoded vectors within a set of selected clusters & Unpacks and store in the buffer

## Slide 28: ANNA: Specialized Architecture for ANNS
Compute Unit (CU)
Compute Unit (CU) 1
Memory Reader
Encoded
Vector
Buffer
Register
Encoded Vector Fetch
Module (EFM)
Memory Reader
Memory Reader
metric
0
Codebook
query
SRAM
To/From MAI
Arb
Compute Unit (CU) 0
Reduction
Unit
Unpacker
Top k
Unit
Top k
Unit
Cluster/Codebook Processing Module (CPM)
Similarity Computation Module
(SCM)
…
Lookup
Table
MAI (Memory Access Interface)
Search Process: Step 3 – Similarity Computation Using Memoization
3. [SCM] Values are fed to the Reduction Unit & Only for Inner Product Add term to the outcome
2. [SCM] Reads encoded identifies & Retrieve value from the Lookup Table
1. [EFM] Loads encoded vectors within a set of selected clusters & Unpacks and store in the buffer

## Slide 29: ANNA: Specialized Architecture for ANNS
Compute Unit (CU)
Compute Unit (CU) 1
Memory Reader
Encoded
Vector
Buffer
Register
Encoded Vector Fetch
Module (EFM)
Memory Reader
Memory Reader
metric
0
Codebook
query
SRAM
To/From MAI
Arb
Compute Unit (CU) 0
Reduction
Unit
Unpacker
Top k
Unit
Top k
Unit
Cluster/Codebook Processing Module (CPM)
Similarity Computation Module
(SCM)
…
Lookup
Table
MAI (Memory Access Interface)
1. The outcome of Reduction Unit is passed to the Top-k Selection unit.
2. Final top-k selected vectors are stored in the memory as the final outcome for the query
Search Process: Step 4 – Top-k Selection

## Slide 30: ANNA Memory Traffic Optimization
Load
Process
(, )
Load
Process
(, )
Load
Process
(, )
Load
Process
(, )
Load
Process
(, )
Load
Process
(, )
Load
Process
(, )
Load
Process
(, )
Cluster 0 , Cluster 1 , , Cluster 2 , ,
Load
Load encoded vectors that belong to cluster
Process
(, )
Compute approximate similarity for encoded vectors in cluster
Baseline ANNA Execution
Example.
ANNA with Memory Traffic Optimization
Load
Process
(, )
Process
(, )
Load
Process
(, )
Process
(, )
Process
(, )
Load
Process
(, )
Process
(, )
Process
(, )
Remove redundant load from the memory
 Memory traffic ↓

## Slide 31: Evaluation
Dataset |  |  | Metric
SIFT1M | 1M | 128 | L2 Distance
Deep1M | 1M | 96 | L2 Distance
GloVe | 1M | 100 | Inner Product
SIFT1B | 1B | 128 | L2 Distance
Deep1B | 1B | 96 | L2 Distance
TTI1B | 1B | 128 | Inner Product
Dataset |  |  | Metric
SIFT1M | 1M | 128 | L2 Distance
Deep1M | 1M | 96 | L2 Distance
GloVe | 1M | 100 | Inner Product
SIFT1B | 1B | 128 | L2 Distance
Deep1B | 1B | 96 | L2 Distance
TTI1B | 1B | 128 | Inner Product
Compression Ratio | Algorithm | Platform |  | 
4:1 | ScaNN16 (CPU) | CPU | 16 | 
 | Faiss16 (CPU) | CPU | 16 | 
 | Faiss256 (CPU) | CPU | 256 | 
 | Faiss256 (GPU) | GPU | 256 | 
8:1 | ScaNN16 (CPU) | CPU | 16 | 
 | Faiss16 (CPU) | CPU | 16 | 
 | Faiss256 (CPU) | CPU | 256 | 
 | Faiss256 (GPU) | GPU | 256 | 
Compression Ratio | Algorithm | Platform |  | 
4:1 | ScaNN16 (CPU) | CPU | 16 | 
 | Faiss16 (CPU) | CPU | 16 | 
 | Faiss256 (CPU) | CPU | 256 | 
 | Faiss256 (GPU) | GPU | 256 | 
8:1 | ScaNN16 (CPU) | CPU | 16 | 
 | Faiss16 (CPU) | CPU | 16 | 
 | Faiss256 (CPU) | CPU | 256 | 
 | Faiss256 (GPU) | GPU | 256 | 
CPU 8-core Intel i7-7820X with 128GB memory
GPU NVIDIA V100 GPU with 32GB memory

## Slide 32: Evaluation – Throughput Improvement

## Slide 33: Evaluation – Latency Improvement
ANNA achieves 24x latency improvements on average across all configuration

## Slide 34: Evaluation – Area and Energy
ANNA is 151x smaller than CPU die size
ANNA is 517x smaller than GPU die size
Module Name | Area (mm2) | Peak Power (W)
Codebook/Cluster Processing Module | 1.17 | 0.391
Encoded Vector Fetch Module | 2.87 | 1.065
Similarity Computation Module (16x) | 13.30 | 3.795
Memory Access Interface (MAI) | 0.17 | 0.147
ANNA Accelerator | 17.51 | 5.398
ANNA Accelerators (12x) | 210.12 | 64.776
ANNA achieves 97x+ energy efficiency improvements over both CPU and GPU

## Slide 35: ANNA: Specialized Architecture for Approximate Nearest Neighbor Search
Yejin Lee | Hyunji Choi | Sunhong Min | Hyunseung Lee
yejinlee@snu.ac.kr | hyunjichoi@snu.ac.kr | sunhongmin@snu.ac.kr | hs_lee@snu.ac.kr
Sangwon Beak | Dawoon Jeong | Jae W. Lee | Tae Jun Ham
bsw1907@gmail.com | daun20211@snu.ac.kr | jaewlee@snu.ac.kr | ham.taejun@gmail.com
Please contact to the author or refer to the full paper for more details
http://arc.snu.ac.kr/pubs/hpca22_anna.pdf